## Slide 1: TURBO TEAM
Amr Khaled Sedik Mohamed Abdelhay
Mohamed Nabil Peter George
Ahmed Abd Aziz Essam Mohamed
Team Members
Notes: Intro: this deck walks through the Main ESP32 firmware that drives a 4WD robot from a web dashboard, with an autonomous mode that keeps it from driving off track edges, plus the camera link and the gripper.

## Slide 2: ESP32 4WD Robot
A complete code walkthrough
Control • Dashboard • Autonomous
Camera • Gripper
LOW-LATENCY / RELIABLE VERSION
Notes: Intro: this deck walks through the Main ESP32 firmware that drives a 4WD robot from a web dashboard, with an autonomous mode that keeps it from driving off track edges, plus the camera link and the gripper.

## Slide 3: System Map
Dashboard
Phone / Laptop
Main ESP32
Access Point
ESP32-CAM
AI-Thinker
Laptop
Edge Impulse
WebSocket :81 + HTTP :80
UART 115200
Wi-Fi /capture
Laptop → robot: GET /detection
The Main ESP32 directly drives:
4 motors (H-Bridge)
Gripper (servo)
4 ultrasonic sensors
Notes: The Main ESP32 is the Wi-Fi access point (192.168.4.1). The dashboard talks to it over WebSocket for real-time control. The camera talks to it over UART for commands and its IP, and sends images to the laptop over Wi-Fi. The laptop runs inference and reports the result back with a /detection request.

## Slide 4: Network & Connectivity
6
Wi-Fi channel
81
WebSocket port
80
HTTP port
4
Max clients
Fixed Access Point: SSID ESP32_Turbo at 192.168.4.1
Lowest latency: Wi-Fi sleep off and max TX power
AP+STA mode with a locked channel (use 1, 6 or 11)
Notes: The robot creates an access point named ESP32_Turbo. The dashboard page is served on port 80 and the WebSocket runs on port 81. Low-latency settings: WiFi.setSleep(false), esp_wifi_set_ps(WIFI_PS_NONE) and esp_wifi_set_max_tx_power(78).

## Slide 5: Control
01
Motors • Steering • WebSocket commands
Notes: Part one: how the robot moves and receives commands.

## Slide 6: Motor Control
Top view (F = forward pin, B = backward pin)
LF
22 / 23
RF
4 / 16
LR
25 / 26
RR
17 / 18
Each motor has two pins: forward and reverse (H-Bridge)
Speed via analogWrite PWM, from 0 to 255
Turn in place: one side forward, the other reverse (tank turn)
Default speed is 255, changed with the SPD:n command
Notes: Each motor is wired to two pins on the H-Bridge (forward and reverse). setMotor() writes PWM to both. LF = 22/23, LR = 25/26, RF = 4/16, RR = 17/18.

## Slide 7: Steering & Failsafe
F
All wheels forward
B
All wheels backward
L
Left reverses, right goes forward
R
Right reverses, left goes forward
45%
Combined steering FL / FR / BL / BR: the inner side slows to 45% of speed instead of reversing (STEER_RATIO)
450ms
Failsafe: if no new command arrives within 450 ms, the robot stops by itself (CONTROL_TIMEOUT)
Notes: The combined commands FL/FR/BL/BR slow the inner side to 45% of speed. Any movement command has to keep arriving: if 450 ms pass with nothing new, stopAll() runs. This protects the robot if the connection drops.

## Slide 8: WebSocket Commands
Movement
F B L R S FL FR BL BR
Speed
SPD:200 (0 - 255)
Autonomous
AUTO:ON AUTO:OFF
Camera
CAM:ON CAM:OFF FLASH:ON FLASH:OFF
Gripper
GRIP:OPEN GRIP:CLOSE
System
HELLO → status PING:t → PONG:t
Notes: All commands are short text messages on the WebSocket (port 81). S is always allowed, even in AUTO mode, and it exits AUTO. Other movement commands are ignored while autonomous mode is running.

## Slide 9: Dashboard
02
An HTML page stored in PROGMEM and served by the ESP32
Notes: Part two: the interface you drive the robot from.

## Slide 10: Dashboard Components
Robot status
Current state plus WS, RTT and client count
Speed
Slider from 0 to 255 with + and − buttons
Arrow controls
Press and hold arrows, plus a red STOP button
Control direction
Reverse button swaps forward and backward
Autonomous
ON / OFF and the four sensor readings
Camera + gripper
Camera, flash, detection result, grip open / close
Notes: The dashboard is a single page embedded in the code (MAIN_page) and served at /. It has cards for status, speed, arrows, control reversal, autonomous mode, camera, the Edge Impulse result and the gripper.

## Slide 11: Keyboard Shortcuts
← ↑ ↓ →
Move the robot
SPACE
Emergency stop
G
R
Gripper: open / close
C
D
Camera: on / off
E
W
Flash: on / off
V
Reverse controls
A
Q
Autonomous: on / off
+
−
Speed: up / down
Notes: Red keys stop things (SPACE and Q). Yellow keys are everything else. Arrow keys can be combined (for example up + left) for combined steering.

## Slide 12: Dashboard ⇄ Robot
1
Auto-connect
WebSocket on port 81, retry every 300 ms
2
Commands
Sent on change, plus a keepalive every 100 ms
3
Live status
Status JSON every 50 ms, RTT every second
4
Page safety
Losing focus or hiding the tab sends S
Status JSON example
{"robot":"AUTO FORWARD","auto":true,"autoState":"FORWARD",
"lf":24.1,"rf":24.3,"ls":18.7,"rs":18.9,"lfGap":false,...}
Notes: The dashboard sends a command when it changes and again every 100 ms while a button is held, because the robot stops if 450 ms pass without a command. The robot pushes a JSON status every 50 ms.

## Slide 13: Autonomous
03
Raised track, no walls: don’t fall off the edge
Notes: Part three: the self-driving mode.

## Slide 14: How Autonomous Works
edge
edge
LF
RF
LS
RS
The hazard is the edge, not a wall: no wall following
4 HC-SR04 sensors aim at the ground: front LF/RF, side LS/RS
ECHO must drop from 5 V to 3.3 V (2k / 3.9k divider)
On AUTO start, each sensor learns the normal ground distance
LF 27/34 · RF 19/35 · LS 14/36 · RS 13/39
Notes: The track is raised and has no walls, so the edges are the hazard. The sensors point down at the ground. The numbers in the last box are TRIG/ECHO pins for each sensor. Dropping ECHO from 5 V to 3.3 V is essential.

## Slide 15: Filtering & Calibration
1
Calibrate
5 readings set the ground baseline
2
Median-of-5
Median of the last 5 readings removes spikes
3
Delta
Reading minus baseline; a rise means an edge
4
Hysteresis
Warning clears only 1.5 cm below the limit
5 / 10 cm
Front sensor: warn / danger
4 / 8 cm
Side sensor: warn / danger
× 2
Two no-echo reads = danger
Notes: Each sensor is calibrated against the normal ground distance (the first 5 valid readings under 150 cm, taken while stopped). Danger is decided by the difference from that baseline, not by a fixed distance. Two no-echo reads in a row count as an edge, because the ground has disappeared.

## Slide 16: Autonomous States
CALIBRATING
Calibrates while stopped
FORWARD
Drives at speed 170
BRAKING
Brake for 80 ms
TURN L / R
Turn 180-420 ms
Sensors ready
Front edge
After 80 ms
Turn done and path clear: back to FORWARD
HAZARD STOP
From any state: stale sensor • two edges at once • turn over 420 ms. Stays stopped until AUTO OFF.
Notes: After calibration the robot enters FORWARD. If a front edge appears it brakes for 80 ms, then turns away from the edge (edge on the left means turn right, and the other way round). After the turn it returns to FORWARD. Any dangerous situation goes to HAZARD STOP, a terminal state until you switch autonomous mode off and on again.

## Slide 17: Decision Priority
1
Stale sensor (over 220 ms) or not calibrated → HAZARD STOP
2
Both front edges (after 80 ms) or both side edges → HAZARD STOP
3
While turning: if an edge shows on the turn side, reverse the turn
4
Front edge on LF or RF → brake 80 ms, then turn away from it
5
Side edge → steer away from it (inner side at 35% speed)
6
Side warning → gradual steering; both sides → speed 120, otherwise 170
Notes: This is the order of checks in autonomousService(): safety first, then the front edge, then side edges, and gradual steering last. Number 1 has the highest priority.

## Slide 18: Safety Layers in Numbers
220ms
Max sensor reading age before stopping
450ms
Control command timeout before stopping
80ms
Confirmation time for a double front edge
420ms
Max duration of a single turn
4s
Camera link timeout (NO LINK)
35%
Autonomous steering ratio (0.35)
Notes: Safety comes in layers: sensor reading expiry, command timeout, confirmation time, a turn time limit and the camera timeout. Manual steering is unchanged; autonomous mode uses its own 0.35 ratio.

## Slide 19: Camera & Gripper
04
UART • Edge Impulse • Servo
Notes: Part four: the camera and the gripper.

## Slide 20: Camera UART Link
Wiring
MAIN GPIO32 TX → CAM GPIO3 RX
MAIN GPIO33 RX ← CAM GPIO1 TX
MAIN GND → CAM GND
Baud 115200
Protocol
Main → Cam : CAM_ON | CAM_OFF
FLASH_ON | FLASH_OFF
Cam → Main : CAM_STATE:ON/OFF
CAM_FLASH:ON/OFF
CAM_IP:192.168.4.X
400ms
Command retry interval
10
Max tries, then NO LINK
4s
Heartbeat timeout
Notes: Commands between the Main ESP32 and the camera travel over UART. The camera reports its DHCP IP so the laptop knows where to request /capture. The Main resends an ON/OFF command every 400 ms up to 10 times, and restores the desired state automatically if the camera reboots.

## Slide 21: Shape Detection (Edge Impulse)
Camera
Serves images at /capture
Laptop
Edge Impulse runs inference
Robot
Receives the result at /detection
Dashboard
Shows Pyramid / Cube / Ball
Example request
/detection?label=Pyramid&confidence=0.94&p=0.94&c=0.03&b=0.02
Scores are accepted as 0..1 or 0..100; the dashboard parses P / C / B from the text
Notes: Detection runs on the laptop, not on the robot. The Main only receives the result and stores it in detectionText. The dashboard reads the Pyramid / Cube / Ball scores with a regex from the P:xx C:xx B:xx text.

## Slide 22: Gripper (Servo)
GPIO 21
Servo pin
50 Hz
PWM, 16 bits resolution
5°–180°
Open → close
500–2400
Pulse width in µs
Angle 0–180°
Pulse width µs
duty ÷ 20000µs
ledcWrite
Commands: GRIP:OPEN / GRIP:CLOSE, or the G and R keys. The state (OPEN / CLOSED) shows on the dashboard.
Notes: The gripper runs on LEDC at GPIO 21 with a 50 Hz, 16-bit signal. servoWriteAngle() converts the angle to a pulse width between 500 and 2400 microseconds, then to a duty value.

## Slide 23: Thank You
Made by Amr Khaled Sedik , Computer Engineer